## Slide 1: Ad-hoc On-Demand Distance Vector Protocol (AODV)
Course title:
Wireless & Mobile Networks
Professor:
Dr. Zeinab MOVAHEDI

## Slide 2: AODV Concept
Reactive (on-demand) routing protocol
  Path discovery initialized when a new route is needed
  Nodes not on active paths don’t maintain routing information
Based on bi-directional links
A broadcast route discovery mechanism
  Based on Route Request (RREQ) and Route Reply (RREP) packets
Dynamic establishment & record of route table entries
  A routing table entry is expired if not used recently
  Update routing table through destination sequence#
    Prevention of routing loops
    Avoidance of old and broken routes

## Slide 3: Path Discovery Mechanism Broadcasting RREQ
S
D
Initiated by broadcasting a Route Request (RREQ)
  < broadcast_id, src_addr, src_seq, dest_addr, dest_seq#, hop_cnt>
  broadcast_id incremented when the source sends a new RREQ
The path discovery is initiated when a source needs to communicate with a destination for which it has no route in its table.
Freshness of the forward path to the destination, last known # to the source
To uniquely identify a RREQ
Freshness of the reverse route to the source

## Slide 4: Path Discovery Mechanism Receiving RREQ at intermediate node
If duplicate, drops the RREQ
Else
  If no active route, rebroadcasts the RREQ increasing its hop_cnt
  Otherwise, it sends a Route Reply (RREP) back to source
  Anyway, keeps track of information required for
    identifying the recived RREQ: <src_addr, broadcast_id>
    setting up reverse path: <src_addr, src_seq#, hop_cnt, expiration timer>
      Nodes not along the path determined by the RREP will timeout after ACTIVE_ROUTE_TIMEOUT

## Slide 5: Path Discovery Mechanism Reverse path setup
S
D
Automatically maintained by intermediate node
A pointer to the neighbor from which it received the first copy of RREQ
Valid during ACTIVE_ROUTE_TIMEOUT
  An enough time for RREQ to traverse the network and produce a RREP back to the source

## Slide 6: Path Discovery Mechanism Receiving RREQ at intermediate node with route entry
Checks if RREQ received over bi-directional link
Check if the route is current
dest_seq# in RREQ < dest_seq# in route entry
  No, Rebrodcast RREQ
  Yes, sends RREP back to source
    <src_addr, dest_addr, dest_seq#, hop_cnt, lifetime>

## Slide 7: Path Discovery Mechanism Receiving RREP along the reverse path
If
(the first RREP received) OR
(RREP dest_seq# > route entry dest_seq#) OR
(RREP dest_seq# = route entry dest_seq#) & (RREP hop_cnt < route entry hop_cnt)
  Yes,
    set the forward path pointing to the node from which the RREP comes
    update the ACTIVE_ROUTE_TIMEOUT for reverse and forward path
    records the latest dest_seq# for destination
  No, ignore RREP

## Slide 8: Path Discovery Mechanism Receiving RREP at source
The source node receiving RREP,
  Begins immediately its data transmission
  may later update its route entry based on a new RREP

## Slide 9
B
S
E
C
G
F
A
H
D
Y
I
K
P
L
J
T
Z
RREQ
AODV Example

## Slide 10
B
S
E
C
G
F
A
H
D
Y
I
K
P
L
J
T
Z
Reverse Path Setup
AODV Example

## Slide 11
B
S
E
C
G
F
A
H
D
Y
I
K
P
L
J
T
Z
AODV Example

## Slide 12
B
S
E
C
G
F
A
H
D
Y
I
K
P
L
J
T
Z
AODV Example

## Slide 13
B
S
E
C
G
F
A
H
D
Y
I
K
P
L
J
T
Z
RREP
AODV Example

## Slide 14
B
S
E
C
G
F
A
H
D
Y
I
K
P
L
J
T
Z
Forward path setup
AODV Example

## Slide 15
B
S
E
C
G
F
A
H
D
Y
I
K
P
L
J
T
Z
AODV Example

## Slide 16
B
S
E
C
G
F
A
H
D
Y
I
K
P
L
J
T
Z
AODV Example

## Slide 17
B
S
E
C
G
F
A
H
D
Y
I
K
P
L
J
T
Z
AODV Example

## Slide 18: Route table management
Soft-states associated with each entry
  RREQ expiration timer for reverse path routing entries
    purge related from nodes not lying on the path from source to destination
    depends to the size of MANET
  Route caching timeout
    time after which route considered invalid
    is postponed by active_route_timeout each time entry used for a transmission
  List of active neighbors for that destination
    neighbors originating/relaying at least one packet for that destination within active-timeout period
    to notify all active sources when a link along the path to a given destination breaks
    a route entry is active if it is in use by any active neighbors

## Slide 19: Route table management
Destination | Next hop | Number of hops | Destination Seq # | Active neighbors for this route | Expiration time
  The route entry is updated upon reception of a new RREP for a destination, only if
    the destination seq# in RREP is greater than the one in table
    if equal but the hop count in RREP smaller than the number of hops in table

## Slide 20: Route maintenance
Detect broken link
  Periodic hello messages
  Link Layer Acknowledgement (LLACKS)
Upon detection of a broken link
  The node prior to the broken link propagates an unsolicited RREP to all active upstream neighbors
    destination Seq# one greater than the previously known, hop count
  Nodes receiving this unsolicited RREP relay that packet to their active neighbors, and so one
  When unsolicited RREP reach source nodes, a new RREQ with destination Seq# one greater than the previous one can be initiated if a route to the destination is still needed
    To ensure new viable route, and no nodes reply if still regard the previous route as valid

## Slide 21: Local connectivity management
When receiving a broadcast packet from a neighbor
A node broadcasts locally a hello message (special unsolicited RREP) with its sequence number if does not send any packets to all of its active upstream neighbors within hello_interval
Local connectivity change
  Receving hello or broadcast packet from a new neighbor
  Failing to receive allowed_hello_loss consecutive hello message from an active neighbor
Hello messages are used also to ensure bidirectional connectivity
    Need to be specifically configured to save bandwidth