## Slide 1: Mobile Ad hoc Networks
Course title:
Wireless & Mobile Networks
Professor:
Dr. Zeinab MOVAHEDI

## Slide 2
No cellular infrastructure.
Multi-hop wireless links.
  Data is routed via intermediate nodes.
Host movement frequent.
  Topology change frequent.
Battery constraint
A
B
Mobile Ad Hoc Networks (MANET)
Definition & Challenges
A
B

## Slide 3
Mobile Ad Hoc Networks (MANET)
Applications

## Slide 4: Dynamic Source Routing Protocol
Course title:
Wireless & Mobile Networks
Professor:
Dr. Zeinab MOVAHEDI

## Slide 5: Features of DSR (1)
Specially designed for MANETs
Dynamically discover a source route to any destination.
    Loop free routing
    No routing information in the intermediate nodes
    This routing information can be cached by other nodes forwarding or overhearing any of these packets

## Slide 6: Features of DSR (2)
DSR has been integrated into
  Standard Internet routing, where a gateway connected to the Internet also participates in MANET routing
  Mobile IP routing, where such a gateway node also serves the role of a Mobile IP foreign agent
Supports internetworking between different types of wireless networks
  Allows a source route to be composed of hops over a combination of any types of networks available

## Slide 7
All nodes willing to participate fully in the routing.
Network diameter will often be small (5 to 10 hops).
Moderate nodes speed with respect to the packet transmission latency & wireless transmission range.
  Not making the flooding of every individual data packet the only possible routing protocol.
Each node selects a single IP address.
Assumptions (1)

## Slide 8
Assumptions (2)
Supporting uni-directional link.
  due to differing antenna or propagation patterns or sources of interference around the two nodes
Nodes may be able to enable promiscuous receive mode on their wireless network interface.
  Advantage: routing optimizations
  Disadvantage: CPU overhead & power consumption
A receiving mode in which the hardware delivers every received packet to the network driver software without filtering based on link-layer destination address.

## Slide 9: DSR Mechanisms
Route discovery
Route maintenance
The mechanism by which a node S wishing to send a packet to a destination node D obtains a source route to D.
Route Discovery is used only when S attempts to send a packet to D and does not already know a route to D.
The mechanism by which node S is able to detect, while using a source route to D, if the network topology has changed such that it can no longer use its route to D because a link along the route no longer works.
Route Maintenance is used only when a route is in use

## Slide 10: DSR strengths
Both mechanisms “on-demand”
    No periodic routing advertisement, No link status sensing, No neighbor detection packets
    Low overhead, scalability
Routes caching in many of nodes for each single route discovery or through overhearing
    Rapid reaction to routing changes
    Low overhead

## Slide 11: Basic DSR Route Discovery
S requires a route to D
S searches its route cache to find a source route to D
  If found, it sends its message with the source route in cache
  Otherwise, it initiates a Route Request (RREQ) to dynamically find a new route to D (S: Initiator, D: Target of the Route Discovery)

## Slide 12: Basic DSR Route Discovery RREQ phase (1)
S saves a copy of the original packet in a Send Buffer
S sends a RREQ message
  <Initiator node S, Target node D, Unique request id, A source route record initialized to an empty list by the initiator>
3) RREQ is send as a single local broadcast packet
  Received by (approximately) all nodes currently within wireless transmission range of S

## Slide 13: Basic DSR Route Discovery RREQ phase (2)
When another node receives a RREQ
  if the target of the Route Discovery
      Returns a Route Reply (RREP) to the initiator, giving a copy of the accumulated route record from RREQ.
  Otherwise, if this node has recently seen another RREQ from this initiator with same request id, or if its own address is already listed in the route record in the RREQ, it discards the RREQ.
  Otherwise, this node appends its own address to the route record in the RREQ and propagates it by transmitting it as a local broadcast packet (with the same request id).

## Slide 14: Basic DSR Route Discovery RREP phase (1)
D examines its own Route Cache for a route back to S
  if found, uses it as the source route for delivery of RREP.
  Otherwise,
    Piggybacking RREP in a new RREQ packet for S
    E/D may reverse the route in RREQ, and use this as the source route of the RREP itself (if bidirectional links).
When the initiator receives RREP, it caches this route in its Route Cache

## Slide 15: Basic DSR Route Discovery send buffer (1)
  Send Buffer contains a copy of packets waiting for a source route stamped with the time of placement into the send Buffer
  A packet is discarded from send buffer
    After expiration of the timer
    By a FIFO or other replacement strategy to prevent the Send Buffer from overflowing

## Slide 16: Basic DSR Route Discovery send buffer (2)
Reinitiate a new RREQ for a packet remaining in the send buffer
This RREQ re-initiation should have a limited rate to reduce the overhead of inutile RREQs towards a same target
  since the destination node may not currently be reachable (due to network partitioning)
  RREQs towards a same target should be distanced by an exponential back-off.
  If the node have additional data packets to the same target more frequently than this limit, the subsequent packets should be buffered until a RREP is received.

## Slide 17: Basic DSR Route Discovery example
B
A
S
E
F
H
J
D
C
G
I
K
Represents a node that has received RREQ for D from S
M
N
L

## Slide 18: Basic DSR Route Discovery example
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L
B
A
S
E
F
H
J
D
C
G
I
K
Represents transmission of RREQ
Broadcast
M
N
L
[S]
[X,Y] Represents route record stored in RREQ

## Slide 19: Basic DSR Route Discovery example
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L
[S,E]
[S,C]
[S,B]
Node H receives packet RREQ from two neighbors:
potential for collision

## Slide 20: Basic DSR Route Discovery example
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L
C receives RREQ from G and H, but does not forward
it again, because C has already forwarded RREQ once
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L
[S,C,G]
[S,E,F]
[S,B,A]
[S,B,H]

## Slide 21: Basic DSR Route Discovery example
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L
J and K both broadcast RREQ to D
Their transmissions may collide at D
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L
[S,C,G,K]
[S,E,F,J]
[S,B,H,I]

## Slide 22: Basic DSR Route Discovery example
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L
B
A
S
E
F
H
J
D
C
G
I
K
D does not forward RREQ, because D is the intended target
M
N
L
[S,E,F,J,M]
D does not forward RREQ, because D is the intended target

## Slide 23: Basic DSR Route Discovery example
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L
RREP [S,E,F,J,D]
Represents RREP control message

## Slide 24: Additional Route Discovery features Caching extra routing information
Caching forwarding/overheard routing information
  Source route in data packet
  Accumulated route in RREQ
  Route returned in RREP
Considering uni-directional links

## Slide 25: Additional Route Discovery features Replying to RREQ using cached routes
The intermediate node must verify that the resulting route being returned contains no duplicate nodes listed in the route record
  To ensure that RRER achieves all intermediate nodes
  Next RREQ not contaminated by RREP with the same stale route
The route record in RREP, concatenation of
  Route over which this copy of RREQ was forwarded to it
  The route in its cache from itself to the target

## Slide 26: Additional Route Discovery features Preventing Route Reply storms
Many RREP could be send to A from A’s neighbors
  bandwidth waste & local congestion
A node sends RREP only if it does not overhear within a time that the originator begining a data transfer using a shorter route
  delay random period d = H(h - 1 + r)
    expires faster for nodes with shorter route
  requires the promiscuous mode

## Slide 27: Additional Route Discovery features Route Request Hop Limit
  Limiting the number of allowed hops for RREQs
    Non-propagating RREQ (hop limit = 0)
      determining if the destination is a neighbor of originator
      using a neighbor cache as an extension of the originator cache
    Expanding ring search
      non-propagating RREQ
      hop limit = 1
      hop limit doubled if no RREP
      increases the average latency

## Slide 28: Basic DSR Route Maintenance (1)
Node transmitting the packet responsible for confirming the packet reception by next hop
Receipt confirmation
  At no cost to DSR
    lower layer protocol MAC (Link layer acknowledgment frame defined by IEEE 802.11)
    Passive acknowledgment – overhearing
  DSR-specific software ack
    A bit set to packet header to request such an ack

## Slide 29: Basic DSR Route Maintenance (2)
No receipt confirmation after the maximum number of retransmission
    Route Error (RERR) message to the original sender identifying the broken link
    Upon reception of RERR, the original sender removes this broken link from its cache

## Slide 30: Basic DSR Route Maintenance (3)
When S receives a RERR
  S can attempt to use any other route it happens to know to D
  S can invoke Route Discovery again to find a new route

## Slide 31: Additional route maintenance features packet salvaging
Salvage the data packet causing the RERR to avoid discarding it
  Method 1
    possible routing loop (avoided by marking
    the salvaged packets to prevent from being
    salvaged multiple times)
  Method 2
    no routing loop (source route rules verified)
    back-tracking not possible

## Slide 32
Automatically shortening a source route in use if one or more intermediate hops in the route become no longer necessary
Additional route maintenance features
Automatic Route Shortening

## Slide 33
Prevent stale information in caches of nodes around the source from generating RREPs with the same invalid link
Additional route maintenance features increasing spreading of RERR (1)

## Slide 34
Node S receiving the RERR forwards the RERR over the same source route resulted in RERR.
  Guarantee that the RERR reaches the node generating the RREP containing the broken link.
  Prevent the contamination of a future Route Discovery with the same broken link.
Additional route maintenance features increasing spreading of RERR (2)

## Slide 35
Caching the negative information of a broken link (or highly variable link) during an expiration timer instead of just removing entries with the broken/variable link from its route cache
  Do not accept RREPs containing the bad link
Expiration timer allows reusing links beginning to work again
Additional route maintenance features
caching negative information

## Slide 36
Support for heterogeneous networks
  A subset of nodes with two types of interfaces
    short range & long range (generally lower speed)
    e.g. a group of soldiers communicating among themeselves using short-range radios and with other groups through truck-mounted higher power radios
      communicating with nodes further away without requiring large number of hops
      span gaps between different groups to avoid network partition

## Slide 37
  Each node chooses only one of its interfaces as home address
    treat the overall network as a single routing domain
    interfaces distinguished using a locally unique interface index
    interface index as part of each hop in the sourece route ( indicates that the node must transmit packet using network interface to deliver the packet to the next hop )
      Source route: A/1→B/1→C/4→D/1 Reverse route: D/1→C/4→B/2→A/1
Support for heterogeneous networks

## Slide 38
  Seamless interoperation between MANET and Internet
    allow transparent routing of packets between MANET and Internet
    Support the mobility of nodes between MANET and Internet
    one or more gateway nodes
      nodes in MANET connected also to Internet which participate in MANET through DSR and in Internet through IP routing
        dynamically enlarge the coverage range around a wireless Internet base station through MANET
        act as a Mobile IP home/foreign agent
Internet interconnection and Mobile IP (1)

## Slide 39
  2 special reserved interface indexes for gateway nodes
    Gateway node with two separate physical interfaces
      reserved interface indexes identify the physical Internet interface
    Gateway node with single physical network interface
      reserved interface indexes identify the logical Internet interfaces
  Interface index value for a network interface of a gateway node
    if a Mobile IP mobility agent on that interface: IF_INDEX_MA
      Allow mobility agents to advertise their existence with no cost
      A node receiving a routing header containing the interface index IF_INDEX_MA can send a unicast Mobile IP Agent SOLICITATION to the corresponding address in the routing header to obtain complete information about Mobile IP services
    otherwise: IF_INDEX_Router
Internet interconnection and Mobile IP (2)

## Slide 40
  When a gateway node receives a RREQ
    generates a RREP with its reserved interface index to Internet if it belives it can reach the destination through its Internet connection
    originator may receive a RREP from both the gateway and the destination if it is present in the MANET
    originator should prefer cached routes not traversing a hop with interface index IF_INDEX_MA or IF_INDEX_ROUTER
Internet interconnection and Mobile IP (3)

## Slide 41
DSR piggybacks the data of the multicast application inside a RREQ targeted at the multicast address
  the RREQ is propagated to all nodes within the specified hop count (TTL) of the originator
  each receiving node individually examines the destination address of the packet and discards the packet if this node is not subscribed to that multicast address
An approximation of multicast routing
  Does not support pruning of the broadcast tree to conserve network resources
Multicast routing with DSR

## Slide 42
Simulation
  ns-2
DSR Evaluation
Parameter | Value
Number of nodes | 50
Simulation area | 1500*300 m2
Number of connections | 10, 20, 30
Traffic type | CBR
Traffic rate | 4 packets/s
Simulation time | 900 s
Mobility model | RWP
Nodes speed | 1 m/s, 20 m/s
Radio characteristics | Lucent WaveLAN
MAC layer | IEEE 802.11
Number of runs | 10

## Slide 43
DSR Evaluation: simulation results

## Slide 44
DSR Evaluation: simulation results

## Slide 45
DSR Evaluation: testbed scenario
freeBSD version of Unix
DSR packets encoded as option of IP header
Carnegie Mellon University
Daily during 4 months
5 mobile nodes moving at 10 m/s in an area open to other vehicles with several stop signes
2 stationary nodes separated by 700 m (3 hops)
Bulk file transfer, telnet, CBR (video & voice), real-time position reporting packets

## Slide 46
OPEN DISCUSSION
DYNAMIC SOURCE ROUTING
(DSR) PROTOCOL